## Slide 1
Internetworking with TCP/IP
Lecture 2: Internet Protocol IPv4
Dr. Nazrul Islam
Associate Professor
Department of Information and Communication Technology (ICT)
Mawlana Bhashani Science and Technology University
Tangail-1902, Bangladesh.
Notes: 1

## Slide 2
Outline
Introduction
Internetworking Issues
IPv4
Service Model
IPv4 Datagram Format
IP Service Primitives
IPv4 Addressing
Classless Addressing
Subnetting and Supernetting
Datagram Delivery
Finding the Local Router
Routers
ICMPv4
Address Translation
Datagram Delivery
2

## Slide 3
Introduction
Definition Internetworking
  Interconnection of multiple networks into an Internet
Task: getting packets from the source to destination
In order to achieve the goal, one needs to
  Have knowledge about the topology of the network and also about the network itself
  Be able to select appropriate path through the network
  Select routes to avoid congestion
  Be able provide internetworking when the source and destination are in different networks
Some definitions
  Data Terminal Equipment (DTE): End System (ES) or Host
  Data Communication System (DCS)
  Internetwork (or Internet): composite network being used (e.g., LAN/WAN/LAN)
  Subnetwork: constituent network of the Internet (e.g., LAN)
  Intermediate System (IS) or Interworking Unit (IWU): device that interconnects two networks (e.g., bridge, router, gateway)
3

## Slide 4
Interworking Issues
Functions
  TCP: e2e error and flow control
  IP: routing and forwarding
  NAP: forwarding (only within subnetwork); point-to-point error and flow control;
4

## Slide 5
Internetworking Issues (cont)
Some of the most important issues
  Overall requirements
  Services provided to transport layer
  Naming
  Addressing
  Routing
  Internetworking
  Quality of Service (eventually)
  Maximum packet size
  Flow and error control (at DLL and TL only; not at IP)
  Congestion control
  Error reporting
  Network layer structure
  Architectural approaches
  …
5

## Slide 6
Interworking Issues (cont)
6
Fig 7.1 – Forouzan 4th edition

## Slide 7
Internetworking Issues (cont)
7
Internet network layer
IP adjunct protocols

## Slide 8
IPv4
Two main components
  IP services (IP to/from TCP/UDP)
  Protocol format and mechanisms
Aspects considered
  Service model
  IPv4 datagram format
  IP service primitives
  IPv4 addressing
  Subnets and subnet masks
  Special purpose addresses
  Segmentation and reassembly
  ICMPv4
  Address translation
  Finding the local router
  Datagram delivery
  Generic router architecture
Important addresses
  RFC editor homepage http://www.rfc-editor.org
  RFC hypertext archive http://rfc.dotsrc.org/
  InterNIC (Internet Domain Name Registration Services) http://www.internic.net/
  IANA (Internet Assigned Numbers Authority) http://www.iana.org
  ICANN (Internet Cooperation for Assigned Names and Numbers) http://www.icann.org
8

## Slide 9
Service Model
IP service model
  Best-effort, connectionless service, i.e., no guarantees, only datagram delivery
Main components
  Addressing scheme
  Datagram model of data delivery
Main IP Specs
  IPv4: RFC 791 (1981)
  ICMP: RFC 792 (1981)
  ARP (Ethernet): RFC 826, 1027 (1982)
  RARP (Ethernet): RFC 903 (1982)
ARP/RARP
  There are more versions ARP/RARP, depending upon the network below
  ARP cache: contain address mappings IP address vs. PHY address
9

## Slide 10
IPv4 Datagram Format
10
Fig 7.2 – Forouzan 4th edition

## Slide 11
IPv4 Datagram Format (cont)
Version (4 bits): indicates protocol version number (IPv4; IPv6)
Header Length (HLEN – 4 bits): length of header in 32-bit words
Differentiated Services (DS), previously called Service Type (ST)
  DS: first 6 bits make up the code point subfield, and the last 2 bits are not used
  ST: first 3 bits are called “Precedence” bits, the next 4 bits are called “Type of Service (ToS)” and the last bit is not used
Total Length (16 bits): total datagram length, including the header (max 65,535 bytes)
Identification (16 bits): used to manage the segmentation/reassembly process
Flags (3 bits): only two bits (“More” and “Don’t Fragment”) are currently used to manage the segmentation/reassembly process
Fragment Offset (13 bits): indicates position where in the original datagram the specific fragment belongs; measured in 64-bit units
Time to Live (8 bits): TTL specifies how long (in sec), a datagram is allowed to remain in the Internet; decreased each time the datagram passes a router (1 sec/router)
Protocol (8 bits): indicates the higher layer protocol to received the data field (at destination) – RFC 1700
Header Checksum (16 bits): an error-detecting code is applied in the IP header only; this code is verified and recomputed at every router
Source Address (32 bits): to allow a variable number of bits to specify the network (and the subnetwork) and the host address of the transmitting host
Destination address (32 bits): to allow a variable number of bits to specify the network (and the subnetwork) and the host address of the receiving host
Options (variable): rarely used today, it allows an IP header to be extended with diverse options, e.g., security, source routing, route recording, stream identification; time stamping
Padding (variable): used to ensure that the datagram header has a length that is multiple of 32 bits
Data (variable): must have a length that is an integer multiple of 8 bits; maximum length is 65,536 octets
11

## Slide 12
IPv4 Datagram Format (cont)
12
Fig 7.3 – Forouzan 4th edition
Table 8.1 – Forouzan 3rd edition
Table 8.2 – Forouzan 3rd edition
Service Type

## Slide 13
IPv4 Datagram Format (cont)
13
Fig 7.6 – Forouzan 4th edition
Table 8.5 – Forouzan 3rd edition
Datagram Maximum Transfer Unit

## Slide 14
IPv4 Datagram Format (cont)
14
IP components
Fig 7.29 – Forouzan 4th edition

## Slide 15
IP Service Primitives
15

## Slide 16
IPv4 Addressing
An IP address is a 32-bit address that uniquely and universally defines the connection of a host or a router to the Internet
IP addresses are unique in the sense that each address defines one, and only one, connection to the Internet
The address space of IPv4 is 232 or 4,294,967,296
Two categories of IP addressing
  Classful addressing
  Classless addressing
16

## Slide 17
IPv4 Addressing (cont)
Class A: 1.0.0.0 to 127.255.255.255 (7 bits for Netid and 24 bits for Hostid; 126 network addresses: 1 – 126; 0 and 127 are reserved; max 16,777,214 hosts/net)
Class B: 128.0.0.0 to 191.255.255.255 (14 bits for Netid and 16 bits for Hostid; 214 = 16,384 network addresses; max 65,534 hosts/net)
Class C: 192.0.0.0 to 223.255.255.255 (21 bits for Netid and 8 bits for Hostid; 221 = 2,097,152 network addresses; max 255 hosts/net)
Class D: 224.0.0.0 to 239.255.255.255 (228 network addresses) [RFC 1112]
Class E: 240.0.0.0 to 247.255.255.255
Special addresses
  0.0.0.0 – some unknown host (booting purposes)
  10.0.0.1 – ARPA NIC (old)
  127.0.0.0 – this host (local loop)
  255.255.255.255 – any host (broadcast purposes)
  A.255.255.255 – direct broadcast (class A)
  B.B.255.255 – direct broadcast (class B)
  C.C.C.255 – direct broadcast (class C)
17
Netid and hostid
Fig 5.8 – Forouzan 4th edition
Address format: Prefix/Network/Host
Dotted decimal representation: xxx.yyy.zzz.vvv (x, y, z and v between 0 and 9)

## Slide 18
IPv4 Addressing (cont)
18
Fig 5.6 – Forouzan 4th edition
Fig 5.7 – Forouzan 4th edition
Finding the class in binary notation
Finding the address class

## Slide 19
IPv4 Addressing (cont)
The network address is assigned to organization
The range of addresses can automatically be inferred from the network address
19
Finding the class in decimal notation
Fig 5.6 – Forouzan 4th edition

## Slide 20
IPv4 Addressing (cont)
20
Blocks in class A
Blocks in class B
Blocks in class C
Fig 4.7 – Forouzan 3rd edition
Fig 4.8 – Forouzan 3rd edition
Fig 4.9 – Forouzan 3rd edition

## Slide 21
IPv4 Addressing (cont)
Multicast addresses
21
Category addresses
Addresses for conferencing
Table 4.6 – Forouzan 3rd edition
Table 4.5 – Forouzan 3rd edition

## Slide 22
Classless Addressing
Big problem related to IP addressing: ROADS (Running Out of Address Space)
Examples: exhaustion of class B address space and explosion of routing table growth triggered by a flood of new class C
Solution advanced by IETF: Classless Inter-Domain Routing (CIDR)
Today, we have therefore two forms of IP addressing
  Classfull addressing: N (Prefix and Netid) is constrained to 8 or 16 or 24 bits only [RFC 1700 and RFC 1117]
  Classless addressing: N can be any number of bits, up to 30 [RFC 1518 and RFC 1519]; used in CIDR
Accordingly, CIDR dotted decimal representation is in the form xxx.yyy.zzz.vvv/ww, where ww indicates the number of leading bits in the 32-bit IP address that constitute the “Network” portion (example 223.1.1.0/24)
Classful addressing is a special case of classless addressing
22

## Slide 23
Classless Addressing (cont)
23
Example
Prefix lengths
Fig 5.5 – Forouzan 3rd edition
Table 5.1 – Forouzan 3rd edition

## Slide 24
Subnetting and Supernetting
A third hierarchical level was introduced in 1984 in the addressing structure, namely subnet
The address format is therefore: Prefix/Network/Subnetwork/Host
The Subnet field can be of any length and it is specified by a 32-bit mask
The IP addresses are therefore designed with two levels of hierarchy
One determines that an address belongs to a subnet by a ”comparison-under-mask” operation (bitwise AND)
The effect of the Subnet Mask is to erase the portion of the Host field, so leaving only the Network number and the Subnetwork number
24
Fig 4.22 – Forouzan 3rd edition

## Slide 25
Subnetting and Suppernetting (cont)
25
Fig 4.20 – Forouzan 3rd edition
Fig 4.21 – Forouzan 3rd edition
A network with two levels of hierarchy (not subnetted)
A network with three levels of hierarchy (subnetted)

## Slide 26
Subnetting and Suppernetting (cont)
26
Default mask and subnet mask
Comparison of a default mask and a subnet mask
Fig 4.24 – Forouzan 3rd edition
Fig 4.25 – Forouzan 3rd edition

## Slide 27
Subnetting and Suppernetting (cont)
In subnetting, one needs the first address of the subnet and the subnet mask to define the range of addresses
In supernetting, one needs the first address of the supernet and the supernet mask to define the range of addresses
The idea of subnetting and supernetting of classful addresses is almost obsolete
27
Comparison of subnet, default and supernet masks
Fig 4.27 – Forouzan 3rd edition

## Slide 28
Subnetting and Suppernetting (cont)
28
Example of subnetting
Fig 5.6 – Forouzan 3rd edition

## Slide 29
Datagram Delivery
29

## Slide 30
Datagram Delivery (cont)
30
Simplified module for forwarding in classful address without subnetting
Fig 6.7 – Forouzan 4th edition
Fig 6.10 – Forouzan 4th edition
Simplified module for forwarding in classful address with subnetting

## Slide 31
Datagram Delivery (cont)
In classful addressing, one can have a routing table with three columns
In classless addressing, one needs at least four columns
31
Common fields in a routing table
Fig 6.18 – Forouzan 3rd edition

## Slide 32
Finding the Local Router
Question: what to do when there are more routers in a network, and not one? To which router send the datagram?
Another question: how to learn the addresses of these routers?
Discovery procedures are used to answer these questions
Discovery procedures
  Static (system manager, difficult)
  Dynamic, by using ICMP messages of type advertisements and solicitations
Advertisements are broadcasted by the routers to the Internet (every 7th minute)
Solicitations: the hosts may trigger the emission of these messages
32

## Slide 33
Routers
33
Router components
Figs 6.22, 6.23 and 6.24 – Forouzan 4th edition

## Slide 34
Switches
34
Crossbar switch
Banyan switch
Figs 6.25 and 6.26 – Forouzan 4th edition

## Slide 35
ICMPv4
Used by hosts, routers and gateways to communicate information to each other, mostly for signaling/diagnostic error conditions; it provides feedback information about network problems [RFC 792]
Most ICMP messages are diagnostic information that is sent back to the source when a router destroys a packet, e.g., when the routing can not be solved (destination unreachable) or when TTL expires (time exceeded) or when a router detects a congestion (source quench)
ICMP also defines an echo function that can be used for testing connectivity (ping)
ICMP is considered as part of IP but architecturally it lies just above IP, as ICMP messages are carried inside IP datagrams
Software that are using ICMP: ping, traceroute
35
ICMP encapsulation
Fig 9.2 – Forouzan 4th edition

## Slide 36
ICMPv4 (cont)
Two categories of ICMP message
  Error-reporting messages: to report problems that a router or destination host may encounter
  Query messages: to get specific information from a router or another host
36
ICMP messages
Table 9.1 – Forouzan 4th edition

## Slide 37
ICMPv4 (cont)
ICMP messages have the format Type/Code/Checksum and also contain the first eight bytes of the IP datagram (together with the Header) that caused the ICMP message to be generated in the first place, such as the sender can determine the packet that caused the error
37

## Slide 38
Address Translation
Translation between IP and MAC address
  Address Resolution Protocol (ARP) IP to MAC [RFC 826]
  Reverse Address Resolution Protocol (RARP) MAC to IP [RFC 903]
ARP lies architecturally bellow IP, as ARP/RARP messages are carried inside MAC frame (as payload)
Variants of ARP/RARP have been defined for different networking technologies, e.g., Ethernet/IEEE 802.3, Token Ring/IEEE 802.5, FDDI, etc
Programs that use ARP: arp (comment: this is an Ethernet broadcast)
Lists of IP/MAC are in Proxy ARP memory (routers/gateways) and ARP cache memory (hosts)
38

## Slide 39
References
Forouzan B.F,”TCP/IP Protocol Suite”, 4th edition, McGraw-Hill, chapters 4, 5, 6, 7, 8, 9, 18
Other useful addresses
39

## Slide 40
40
THANK YOU!