## Slide 1: ICT 2103 Digital Logic Design
Prof. Dr. Muhammad Shahin Uddin

## Slide 2: Number System
Non-Positioned Number System
Positioned Number System
Roman Number
I = 1, V = 5, X = 10, L = 50, C = 100, D = 500, M = 1000.
1999 is MCMXCIX, or M (1000) + CM (1000-100) + XC (100-10) + IX (10-1).

## Slide 3: Number Base Conversions

## Slide 4: Decimal Number System
Base (also called radix) = 10
  10 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9 }
Digit Position
  Integer & fraction
Digit Weight
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 5: Octal Number System
Base = 8
  8 digits { 0, 1, 2, 3, 4, 5, 6, 7 }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 6: Binary Number System
Base = 2
  2 digits { 0, 1 }, called binary digits or “bits”
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Bit x Weight”
Formal Notation
Groups of bits
8 bits = Byte

## Slide 7: Binary Number

## Slide 8: Hexadecimal Number System
Base = 16
  16 digits { 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F }
Weights
  Weight = (Base) Position
Magnitude
  Sum of “Digit x Weight”
Formal Notation

## Slide 9: The Power of 2

## Slide 10: 1.1a Decimal (Integer) to Binary Conversion
Divide the number by the ‘Base’ (=2)
Take the remainder (either 0 or 1) as a coefficient
Take the quotient and repeat the division
Example:

## Slide 11: 1.1b Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example:

## Slide 12: 1.1c Decimal (Fraction) to Binary Conversion
Multiply the number by the ‘Base’ (=2)
Take the integer (either 0 or 1) as a coefficient
Take the resultant fraction and repeat the division
Example:

## Slide 13: 2.1. Decimal to Octal Conversion

## Slide 14
2.2. Octal to Decimal Conversion
Example:

## Slide 15: 3.1. Binary− Octal Conversion

## Slide 16: 3.2. Octal-to-Binary Conversion
Because each octal digit can be represented by a 3-bit binary number, it is very easy to convert from octal to binary..
Octal/Binary Conversion
Octal Digit 0 1 2 3 4 5 6 7
Binary 000 001 010 011 100 101 110 111
Let’s convert the octal numbers 25 and 140.
2 5 1 4 0
010 101 001 100 000

## Slide 17: 4.1 Binary−Hexadecimal Conversion
Prof. Dr. Muhammad Shahin Uddin
Email: muhammad.uddin@northsouth.edu
Out
Ashraful.sarker@nort

## Slide 18: 4.1 Hexadecimal to Binary Conversion
Method 1

## Slide 19: Method 1: Example

## Slide 20
Method 2
Each digit of the given hexadecimal number should be converted to its 4 bit binary equivalent

## Slide 21: 5.1 Octal−Hexadecimal Conversion

## Slide 22: 5.2 Hexadecimal to Octal Conversion

## Slide 23: Decimal, Binary, Octal and Hexadecimal

## Slide 24: Addition
Decimal Binary

## Slide 25: Binary Subtraction

## Slide 26: Binary Multiplication

## Slide 27: Base Conversion
    Examples:
      (11010)2 =( ? )10
      N = 1´24 + 1´23 + 0´22 + 1´21 + 0´20
      = (16)10 + (8)10 + 0 + (2)10 + 0
      = (26)10
      (627)8 = ( ? )10
      N = 6´82 + 2´81 + 7´80
      = (384)10 + (16)10 + (7)10
      = (407)10

## Slide 28: Base Conversion
    Examples:
      (11010)2 =( ? )10
      N = 1´24 + 1´23 + 0´22 + 1´21 + 0´20
      = (16)10 + (8)10 + 0 + (2)10 + 0
      = (26)10
      (627)8 = ( ? )10
      N = 6´82 + 2´81 + 7´80
      = (384)10 + (16)10 + (7)10
      = (407)10

## Slide 29: Base Conversion
    (11010)2 ®( ? )10
    N = 1´24 + 1´23 + 0´22 + 1´21 + 0´20
    = (16)10 + (8)10 + 0 + (2)10 + 0
    = (26)10
    (627)8 ® ( ? )10
    N = 6´82 + 2´81 + 7´80
    = (384)10 + (16)10 + (7)10
    = (407)10

## Slide 30: Base Conversion
    (11010)2 ®( ? )10
    N = 1´24 + 1´23 + 0´22 + 1´21 + 0´20
    = (16)10 + (8)10 + 0 + (2)10 + 0
    = (26)10
    (627)8 ® ( ? )10
    N = 6´82 + 2´81 + 7´80
    = (384)10 + (16)10 + (7)10
    = (407)10

## Slide 31: Examples of Base Conversion (3)
    (315)10 = (473)8
    (315)10 = (13B)16

## Slide 32: Examples of Base Conversion (3)
    (315)10 = (473)8
    (315)10 = (13B)16

## Slide 33: Base Conversion (5)
    (0.479)10 = (0.3651…)8
    MSD 3.832 ¬ 0.479 ´ 8
    6.656 ¬ 0.832 ´ 8
    5.248 ¬ 0.656 ´ 8
    LSD 1.984 ¬ 0.248 ´ 8
    …
    (0.479)10 = (0.0111…)2
    MSD 0.9580 ¬ 0.479 ´ 2
    1.9160 ¬ 0.9580 ´ 2
    1.8320 ¬ 0.9160 ´ 2
    LSD 1.6640 ¬ 0.8320 ´ 2
    …

## Slide 34
Convert decimal 41 to binary. First, 41 is divided by 2 to give an integer quotient of 20 and a remainder of . Then the quotient is again divided by 2 to give a new quotient and remainder. The process is continued until the integer quotient becomes 0. The coefficients of the desired binary number are obtained from the remainders as follows:
Example 1

## Slide 35
Convert decimal 41 to binary. First, 41 is divided by 2 to give an integer quotient of 20 and a remainder of . Then the quotient is again divided by 2 to give a new quotient and remainder. The process is continued until the integer quotient becomes 0. The coefficients of the desired binary number are obtained from the remainders as follows:
Example 1

## Slide 36
Convert decimal 41 to binary. First, 41 is divided by 2 to give an integer quotient of 20 and a remainder of . Then the quotient is again divided by 2 to give a new quotient and remainder. The process is continued until the integer quotient becomes 0. The coefficients of the desired binary number are obtained from the remainders as follows:
Example 1

## Slide 37
Example 2

## Slide 38
Example 2

## Slide 39: Thanks