## Slide 1
Semiconductor Diode Applications

## Slide 2
Semiconductor Diode Applications
One fundamental application of diode is as a rectifier (converts AC waves in to DC).
To create diode logic gates (such as AND or OR gates).
As a clipper that limits or clipped off the voltage beyond the preset value without changing the remaining part of the input waveform.
As a clamper that shifts or alters either positive or negative peak of input signal to desired level.

## Slide 3
How to solve diode circuits
There are different diode circuits such as:
    Series diode circuits
    Parallel diode circuits
    Series-parallel diode circuits
    Rectifier circuits
    Clipper and clamper circuits
    Etc.
Circuit analyzing techniques:
    Exponential model (Load-line analysis)
    Ideal equivalent circuit (1st approximation)
    Simplified equivalent circuit (2nd approximation)

## Slide 4
Exponential diode model
Exponential diode model
  most accurate, the result found by this model is almost similar to that obtained by Shockley's equation.
  most difficult to employ in circuit analysis
    due to nonlinear nature
We use load line (graphical method) to solve exponential model.

## Slide 5: Load-Line Analysis of Diode Circuits
Q-point
IDQ
VDQ
The Q-point, which identifies ID and VD for a particular diode in a given circuit.

## Slide 6: Load-Line Analysis of Diode Circuits
Example: For the series diode configuration of figure (a) and employing the diode characteristics of figure (b), determine
  and
From the result, plot the straight line across ID and VD.
The resulting load line appears in the right figure. The Q points occurred at
VDQ  0.78 V IDQ  18.5mA
VR=IRR=IDQR=(18.5 mA)(0.5k) =9.25 V
Solution:

## Slide 7
Ideal Equivalent Circuit
The diode is on state if;
The current established by the applied sources is such that its direction matches that of the arrow in the diode symbol.

## Slide 8
Ideal Equivalent Circuit
Example: For the series diode configuration of figure (a), determine
  and
For a ideal diode model,
Using equivalent circuit and KVL
Solution:
Forward bias
IR

## Slide 9
Ideal Equivalent Circuit
Example: For the series diode configuration of figure (a), determine
  and
Solution:
Reversed bias
IR
= 0 A
For a ideal diode model,
Using equivalent circuit and KVL

## Slide 10
Simplified Equivalent Circuit
The diode is on state if;
The current established by the applied sources is such that its direction matches that of the arrow in the diode symbol.
VD ≥ 0.7 V for silicon, VD ≥ 0.3 V for germanium, and VD ≥ 1.2 V for gallium arsenide.

## Slide 11
Series Diode Configuration
Example: For the series diode configuration of the following figure, determine VD, VR and ID for forward biasing
Solution:
For a simplified diode model,
Using equivalent circuit and KVL

## Slide 12
Series Diode Configuration
Example: Repeat previous example with the diode reverse. Thus the equivalent circuit is
Solution:
For a ideal diode model,
Using equivalent circuit and KVL

## Slide 13: When to use these models?
exponential model
  low voltages
  less complex circuits
  emphasis on accuracy over practicality
ideal diode model
  high voltages >> 0.7V
  very complex circuits
  cases where a difference in voltage by 0.7V is negligible
Simplified model:
  medium voltages = 0.7V
  more complex circuits
  emphasis on practicality over accuracy

## Slide 14
Series Diode Configuration
If the diode is biased with the voltage source less than VD, the diode also acting like open circuit
Diode Circuit
Diode Characteristic
With biasing less than 0.7V
Equivalent cct

## Slide 15
Series Diode Configuration
Example: Determine Vo and ID for the series circuit below
Using equivalent circuit and KVL
Vo  E  VK1  VK 2  12V  0.7V  1.8V  9.5V

## Slide 16
Example: Determine ID , VD2 and Vo for the circuit below
Since, open circuit,
And using KVL, we have
- =20V-0V-0V=20V
Series Diode Configuration

## Slide 17
Example: Determine Vo, I1, ID1 and ID2 for the parallel diode below
Since the source voltage is greater than the diode then the current flow and the voltage across diode is 0.7V, thus
The current is
Since diodes are similar thus the current will be same, then
Parallel Diode Configuration

## Slide 18
Example: Determine the currents I1, I2 and ID for the network below
Since R1 is // D2 then voltage is same
Applying KVL in loop 1
Therefore,
And
Series-Parallel Diode Configuration

## Slide 19
Solution:
From fig. on the right apply KVL
Vo  E  VD  10V  0.7V  9.3V
Example: Determine Vo and I for network below
and
I
OR GATE
Input |  | Output, Vo
V1 | V2 | 
10V | 0 | 9.3V
0 | 10V | 9.3V
10V | 10V | 9.3V
0V | 0V | 0V
Truth table of OR gate

## Slide 20: AND GATE
Due to forward bias of D2 the output voltage is Vo= 0.7V
From fig. on the right apply KVL
Example: Determine the output level for the positive logic AND gate below
Input |  | Output, Vo
E1 | E2 | 
10V | 0 | 0.7V
0 | 10V | 0.7V
10V | 10V | 10V
0V | 0V | 0.7V
Truth table of AND gate