## Slide 1
Semiconductor Diode Applications

## Slide 2: Rectifier
One of the most important applications of diodes is in the design of rectifier circuits.
Rectifiers convert ac power to dc power.
Rectifiers form the basis for electronic power suppliers and battery charging circuits.
Fig.: Complete power supply with transformer, rectifier, filter, and regulator

## Slide 3
Block diagram of a dc power supply
Step-1: Decrease RMS magnitude of AC wave via power transformer
step -2: convert full-wave AC signal to full-wave rectified signal (still time-varying and periodic)
step -3: employ low-pass filter to reduce wave amplitude by > 90%
step -4: employ voltage regulator to eliminate ripple
step -5: supply dc load .
Notes: The diagrams indicate a “full-wave” rectifier.

## Slide 4: Rectifier
Rectifier are mainly two types:
Half wave Rectifiers
Full wave Rectifiers.
    Bridge rectifier
    Center tap transformer rectifier

## Slide 5: Half-wave Rectifier
Half wave Rectifiers: A rectifier that allows only one-half cycle of an ac voltage waveform to establish a dc level is called half wave rectification.
Hal-wave rectifier circuit with AC input
Rectifier Output for ideal diode
The average voltage,
[since, ]
Therefore, the dc voltage for halfwave rectifier is

## Slide 6
If simplified diode model is employed.
The diode is conducted after the voltage supplied is more than 0.7V as shown below
So peak value of output is reduced, hence the dc voltage will be reduced.
Vdc  0.318Vm  VK 
Effect of Using a Real Diode

## Slide 7
Example: Circuit as below
Sketch the output vo and determine dc level of the output voltage for ideal diode
What is the practical diode
The Vm is increase to 200V
Half-Wave Rectification
(a)
  Ideal diode circuit:
  Vdc 0.318Vm
   0.31820V 
   6.36V
Solution:

## Slide 8: Vdc  0.318Vm  VK   0.31820V  0.7V   6.14V
(b)
Vdc  0.318Vm   0.318200V   63.6V
(C)
Drop about 0.22V or 3.5 %
Vdc  0.318Vm  VK   0.318200V  0.7  63.38V
Drop about 0.22V or 0.35%
(ideal)
(practical)

## Slide 9: Diode Rating
The maximum value of the reverse voltage that a diode can withstand without damaging itself is known as its Peak Inverse Voltage (PIV).
PIV of diode must be greater than the applied voltage
This rating of PIV is given and described in the datasheet provided by the manufacturer.
It is usually prudent to select a diode that has a reverse breakdown voltage at least 20% greater than the expected PIV.
PIV(rating) > Vm for half –wave rectifier

## Slide 10: Half-wave Rectifier
Advantages:
  Simple construction
  Less number of components are required
  Small size
Disadvantages:
  More amount of ripple content
  Transformer utilization factor is very low.
  Rectification efficiency is low
  Generates harmonics
  Low output voltage or current
Applications:
  It is used for applications where constant DC voltage is not very essential
  We can use in the power supplies

## Slide 11
Full-Wave Rectification
Full wave Rectifiers:
  A rectifier that allows full cycle of an ac voltage waveform to establish a dc level is called Full wave rectification.
  Full-wave rectification produces a greater DC output
  Half-wave: Vdc = 0.318Vm
  Full-wave: Vdc = 0.636Vm

## Slide 12: Full-Wave Bridge Rectifier
Four diodes are connected in a bridge configuration
VDC = 0.636Vm
A full-wave rectifier with four diodes that are connected in a bridge configuration.

## Slide 13: Full-Wave Bridge Rectifier
The bridge rectifier circuit.

## Slide 14: Full-Wave Bridge Rectifier
The bridge rectifier circuit.

## Slide 15: Vdc  20.318Vm   0.636Vm
Ideal diode
Practical diode
Vdc  0.636Vm  2VK 
Full-Wave Bridge Rectification
The effect of using a real diode

## Slide 16: Diode Rating
For real diode
For ideal diode

## Slide 17: Full-wave Bridge Rectifier
Advantages:
  No need for center-tapped transformers
  High average output voltage
  Rectifier efficiency is high
  Transformer utilization factor is high
Disadvantages:
  The number of diode is four
  Series connection of TWO diodes will reduce output voltage.
PIV = Vm – VK
Applications:
  Laboratory dc power supplies
  High current power supplies
  Battery charger
  DC power supplies for various electronic circuits

## Slide 18: Center-Tapped Transformer
Center-Tapped Transformer Rectifier
Requires
  Two diodes
  Center-tapped transformer
  Output:
  VDC = 0.636Vm
  PIV > 2 Vm
The above output is for ideal diode

## Slide 19
When instantaneous source voltage is positive, D1 conducts while D2 blocks…
Center-Tapped Transformer
The center tap transformer rectifier circuit.

## Slide 20
when instantaneous source voltage is negative, D2 conducts while D1 blocks
The center tap transformer rectifier circuit.
Center-Tapped Transformer

## Slide 21: Effect of Real Diode
Vdc  0.636Vm  VK 
The effect of using a real diode

## Slide 22: PIV.
 Vm  2Vm
 VR  Vm
PIV  Vsecondary
PIV  2Vm
Apply KVL
Therefore
    For practical diode, PIV for center tap = 2Vm – VK

## Slide 23: Full-wave Rectifier with Center-Tapped Transformer
Advantages:
  Low ripple factor as compared with half-wave rectifier.
  Better rectification efficiency
  Better transformer utilization factor
Disadvantages:
  Since PIV is 2Vm ,size of the diodes is larger and they are most costly
  Cost of center tapped transformer is high
Applications:
  Laboratory dc power supplies
  High current power supplies
  Battery charger
  DC power supplies for various electronic circuits

## Slide 24: Summary of Rectifier Circuits
Vm = peak of the AC voltage.
In the center tapped transformer rectifier circuit, the peak AC voltage is the transformer secondary voltage to the tap.
The above realistic value is true for only silicon diode.
Rectifier | Ideal VDC | Realistic VDC
Half Wave Rectifier | VDC = 0.318Vm | VDC = 0.318Vm – 0.7
Bridge Rectifier | VDC = 0.636Vm | VDC = 0.636Vm – 2(0.7 V)
Center-Tapped Transformer Rectifier | VDC = 0.636Vm | VDC = 0.636Vm – 0.7 V

## Slide 25: Determine the output for the network below and calculate the output dc level and the required PIV of each diode.

## Slide 26: Solution:
D1
D2
For positive half cycle, diode 2 is on and 1 is off, which is shown in the following figure
Equivalent circuit
Redrawn network
Output for positive cycle

## Slide 27: Solution:
Again, for the negative half cycle, diode 1 is on and 2 is off and we get the same result of positive half cycle.
From the 2nd Fig;
Therefore,
3.18V
Vdc
Resulting output
PIV  Vm  5V

## Slide 28: Practical Applications
Rectifier Circuits
  Conversions of AC to DC for DC operated circuits
  Battery Charging Circuits
Simple Diode Circuits
  Protective Circuits against
  Overcurrent
  Polarity Reversal
  Currents caused by an inductive kick in a relay circuit
Zener Circuits
  Overvoltage Protection
  Setting Reference Voltages
28