## Slide 1
Semiconductor Diode Applications

## Slide 2: Clippers
Electronic devices are very sensitive to voltage.
An over-voltage can permanently destroy the electronic devices.
To protect electronic devices, clipper circuits can be used.
Clipping circuit:
  A wave shaping circuit which controls the shape of the output waveform by removing or clipping a portion of the applied wave.
  Half wave rectifier is the simplest example. (It clips negative or positive half cycle).
  Also referred as voltage limiters/ amplitude selectors/ slicers.

## Slide 3: Clippers
Applications:-
  In radio receivers for communication circuits.
  In radars, digital computers and other electronic systems.
  Generation for different waveforms such as trapezoidal, or square waves.
  They are used as noise limiters in FM transmitter

## Slide 4: Clippers
There are 4 types of clipper circuits
  Positive clipper circuits
  Negative clipper circuits
  Biased clipper circuits
  Combinational clipper circuits

## Slide 5: Positive clipper circuits (Series Diode)
In positive clipper, the positive half cycles of the input AC signal is removed.
For positive half cycle
For negative half cycle
Vm

## Slide 6: Positive clipper circuits (Parallel Diode)
In positive clipper, the positive half cycles of the input AC signal is removed.
For positive half cycle
For negative half cycle
Vm

## Slide 7: Negative clipper circuits (Series Diode)
In negative clipper, the negative half cycles of the input AC signal is removed.
For positive half cycle
For negative half cycle

## Slide 8: Negative clipper circuits (Parallel Diode)
For negative half cycle
For positive half cycle

## Slide 9: Biased clipper circuits
Adding a DC source in series with the clipping diode changes the effective forward bias of the diode.
First Consider, when diode is forward bias
For positive half cycle,
For negative half cycle,

## Slide 10: Summary of Clipper Circuits

## Slide 11: Summary of Clipper Circuits

## Slide 12: Clamper Circuits
A circuit that shifts a waveform to a different dc level without changing the appearance of the applied signal.
Note:
Start the analysis of clamping network, by considering that part of the input signal that will forward bias the diode.
During the period that the diode is in the “ON” state, assume that capacitor will charge up instantaneously to a voltage level determined by the network.
Assume that during the period when the diode is in “OFF” state, capacitor will hold on its established voltage level.
Keep in mind the general rule, that
Total swing of total output = Swing of input signal

## Slide 13: Clamper Circuits
Step 1: Consider the cycle that will forward bias the diode.
Apply KVL
Apply KVL
Step 2: Assume that during the period when the diode is in the “off” state

## Slide 14: Biased Clamper Circuits
The input signal can be any type of waveform such as sine, square, and triangle waves.
The DC source lets you adjust the DC camping level.
Step 1: Diode is on for negative cycle
Apply KVL
Apply KVL
Step 2: Diode is off for positive cycle

## Slide 15: Summary of Clamper Circuits

## Slide 16: Zener Diodes
A Zener diode is a heavily doped semiconductor diode which is designed to conduct current in the breakdown region.
Voltage regulation is the most common application of a Zener diode.
A voltage regulator circuit keeps the load voltage constant irrespective changes in input voltage or load resistance.
Symbol of Zener diode
Approximate equivalent circuits for the Zener diode in the three possible regions of application.

## Slide 17: Zener Diodes
Points to be noted:
  In forward bias, it acts as a normal PN junction diode.
  In reverse bias, it conducts current when the voltage across it is equal to or greater than Zener voltage (Vz).
  It regulates the voltage across it which is equal to the Zener voltage.
When Vi  VZ
  The Zener is on
  Voltage across the Zener is VZ
  Zener current: IZ = IR – IRL
  The Zener Power: PZ = VZIZ
When Vi < VZ
  The Zener is off
  The Zener acts as an open circuit

## Slide 18: Zener Diodes
The network of the following figure is designed to limit the voltage to 20 V during the positive portion of the applied voltage and to 0 V for a negative excursion of the applied voltage. Check its operation and plot the waveform of the voltage across the system for the applied signal. Assume the system has a very high input resistance so it will not affect the behavior of the network
For positive cycle
For negative cycle

## Slide 19: Zener Diode as Voltage Regulator
Three conditions are considered to analysis the Zener regulator circuit
      Vi and RL fixed
      Fixed Vi and variable RL
      Variable Vi and RL fixed

## Slide 20: Voltage Regulator Circuit (Vi and RL fixed:)
Step 1: To determine the state of the Zener diode, Apply Thevenin's theorem: remove Zener diode from the network
Case-I: If V≥ VZ, the Zener diode is on,
Case-II: If V<VZ, the diode is off,
For Case-I: If V≥ VZ, the Zener diode is on,
PZ = VZIZ
The power dissipated by the Zener diode is

## Slide 21: Example: a. For the following Zener diode network, determine VL , VR , IZ , and PZ b. Repeat part (a) with RL = 3kΩ.
Step 1: Redraw the circuit by removing Zener diode from the network
Since V=8.73 V is less than VZ =10V, the diode is off state as shown in the following characteristics curve.

## Slide 22: Example: b. Repeat part (a) with RL = 3kΩ.
Step 1: Redraw the circuit by removing Zener diode from the network
Since V =12 V is greater than VZ =10V, the diode is in the “on” state.
The power dissipated by the Zener diode is
PZ that must be less than the PZM =30 mW specified for the device.

## Slide 23: Voltage Regulator Circuit (Vi fixed & RL variable:)
Since, load is variable, we need to find minimum and maximum resistance, which remain the diode is on.
How?
If we consider, , which is less than , so diode is off.
Condition for minimum :
So, to find minimum resistance that will turn diode on, we need to calculate .
,
Condition for maximum :
As we know,
So,

## Slide 24
Solution:
To find minimum resistance that will turn diode on,
Condition for maximum :
As we know,
Example: For the following network:
  determine the range of RL and IL that will result in VRL being maintained at 10 V.
  Determine the maximum wattage rating of the diode.

## Slide 25: Voltage Regulator Circuit (Vi variable & RL Fixed:)
Homework

## Slide 26: AC Regulator
Square Wave Generator