## Slide 1
Field Effect Transistors-FET

## Slide 2: Introduction
IN THIS LECTURE WE WILL LEARN:
  General overview on FET transistor and its types.
  The physical structure of the MOS transistor and how it works.
  How the voltage between two terminals of the transistor control the current that flows through the third terminal, and the equations that describe these current-voltage characteristics.
  How the transistor can be used to make an amplifier, and how it can be used as a switch in digital circuits.

## Slide 3: Introduction
The invention of the BJT has brought a great twist in the modern era of semiconductor technology. This device, along with its field-effect counterpart, known as the field-effect transistor (FET), has had a huge impact on virtually every area of modern life.
Practical field-effect transistors were first made in the form of JFET in 1953 and MOSFET in 1963.
Two main types of FET:
  - JFET –Junction field effects transistor
  MOSFET – Metal oxide semiconductor field effect transistor
    D-MOSFET ~ Depletion MOSFET
    E-MOSFET ~ Enhancement MOSFET

## Slide 4: Differences between FET & BJT
 | Field Effect Transistor (FET) | Bipolar Junction Transistor (BJT)
1 | Unipolar Current depends only on one type of carriers | Bipolar Current depends on both electrons and holes
2 | Voltage controlled device | Current controlled device
3 | Very high input impedance | Low input impedance
4 | Simpler in fabrication and occupies less space in integrated form | occupies large space in integrated form
5 | Low voltage gain High current gain | High voltage gain Low current gain
6 | Easily damaged | Robust

## Slide 5: Similarities between FET & BJT
  Similarities:
    • Amplifiers
    • Switching devices
• Impedance matching circuits

## Slide 6
JFET Construction
There are two types of JFETs
  n-channel
  p-channel
The n-channel is more widely used.
There are three terminals:
  Drain (D) and Source (S) are connected to the n-channel through an ohmic contact
  Gate (G) is connected to the p-type material
  JFET has two p-n junctions under no-bias conditions.

## Slide 7: N-Channel JFET Symbol

## Slide 8
JFET Operation: The Basic Idea
JFET operation can be compared to a water spigot.
The source of water pressure is the accumulation of electrons at the negative pole of the drain-source voltage.
The drain of water is the electron deficiency (or holes) at the positive pole of the applied voltage.
The control of flow of water is the gate voltage that controls the width of the n-channel and, therefore, the flow of charges from source to drain.

## Slide 9: Junction field effect transistor (JFET)
p
p
Gate
Drain
n
Source
Voltage controlled – the gate voltage controls the drain current
VDD
VGG
N-Channel JFET Circuit Layout:

## Slide 10: JFET Operating Characteristics
There are three basic operating conditions for a JFET:
VGS = 0 V (zero), VDS increasing to some positive value
VGS < 0 V (negative), VDS at some positive value
Ohmic region: Voltage-controlled resistor

## Slide 11
JFET Operating Characteristics: VGS = 0 V
  The depletion region between p-gate and n-channel increases as electrons from n-channel combine with holes from p-gate.
  Increasing the depletion region, decreases the size of the n-channel which increases the resistance of the n-channel.
  Even though the n-channel resistance is increasing, the current (ID) from source to drain through the n-channel is increasing. This is because VDS is increasing.
Three things happen when VGS = 0 and VDS is increased from 0 to a more positive voltage
JFET at VGS = 0 V and VDS> 0 V.
Varying reverse-bias potentials across the p–n junction of an n-channel JFET.

## Slide 12
If VGS = 0 and VDS is further increased to a more positive voltage, then the depletion zone gets so large and touch each other that it pinches off the n-channel.
This suggests that the current in the n-channel (ID) would drop to 0A, but it does just the opposite–as VDS increases, so does ID.
Once pinch off occurs, further increases in VDS do not cause ID to increase.
JFET Operating Characteristics: Pinch Off
At the pinch-off point:
VGS at pinch-off is denoted as Vp.
ID is at saturation or maximum. It is referred to as IDSS.
The ohmic value of the channel is maximum.

## Slide 13: At Pinch-Off, The Channel Is Not Really Pinched Off!
The term pinch-off is a misnomer in that it suggests the current ID is pinched off and drops to 0A.
  However, this is hardly the case —ID maintains a saturation level defined as IDSS
In reality, a very small channel still exists, with a current of very high density.
Why zero ID is not possible at pinch-off? The absence of a drain current would remove the possibility of different potentials along the n-channel to establish the varying levels of reverse bias along the p–n junction.
  The result would be a loss of the depletion region
distribution that caused pinch-off in the first place.

## Slide 14
JFET Operating Characteristics, VGS < 0 V (negative),
As VGS becomes more negative, the depletion region begins to increase reducing the overall effective area of the channel and thus reducing the current flowing through it.
As VGS becomes more negative:
The JFET experiences pinch-off at a lower voltage (VP).
ID decreases (ID < IDSS) even though VDS is increased.
Eventually ID reaches 0 A. VGS at this point is called Vp or VGS(off).
Also note that at high levels of VDS the JFET reaches a breakdown situation. ID increases uncontrollably if VDS > VDSmax.

## Slide 15
The region to the left of the pinch-off point is called the ohmic region.
The JFET can be used as a variable resistor, where VGS controls the drain-source resistance (rd). As VGS becomes more negative, the resistance (rd) increases.
JFET Operating Characteristics: Voltage-Controlled Resistor

## Slide 16
p-Channel JFETS
The p-channel JFET behaves the same as the n- channel JFET.
The only differences are that the voltage polarities and current directions are reversed.

## Slide 17
p-Channel JFET Characteristics
Also note that at high levels of VDS the JFET reaches a breakdown situation: ID increases uncontrollably if VDS > VDSmax.
As VGS increases more positively
  The depletion zone increases
  ID decreases (ID < IDSS)
  Eventually ID = 0 A

## Slide 18
JFET Symbol
JFET symbols: (a) n-channel; (b) p-channel.

## Slide 19: JFET Transfer Characteristics
JFET input-to-output transfer characteristics are not as straightforward as they are for a BJT.
BJT:  indicates the relationship between IB (input) and IC
(output).
JFET: The relationship of VGS (input) and ID (output) is a little more complicated:

## Slide 20
JFET Transfer Curve (Transconductance curve)
This graph shows the value of ID for a given value of VGS.
Using IDSS and Vp (VGS(off)) values found in a specification sheet, the transfer curve can be plotted according to these three steps:
Solving for VGS = 0V ID = IDSS
Step 1
Solving for VGS = Vp (VGS(off)) ID = 0A
Step 2
Solving for VGS = 0V to Vp
Step 3

## Slide 21: Equations in active region
is the maximum drain current for a JFET and is defined by the conditions and .
drain current
Source current
Collector current
Emitter current

## Slide 24: Integrated Circuit Operational View of An N-Channel JFET

## Slide 25
MOSFETs
There are two types of MOSFETs:
  Depletion-Type
  Enhancement-Type
MOSFETs have characteristics similar to JFETs and additional characteristics that make then very useful.

## Slide 26: Introduction
Q: What are two major types of three-terminal semiconductor devices?
  metal-oxide-semiconductor field-effect transistor (MOSFET)
  bipolar junction transistor (BJT)
Q: Why are MOSFET’s more widely used?
  size (smaller)
  ease of manufacture
  lesser power utilization
MOSFET technology
  It allows placement of approximately 2 billion transistors on a single IC
    backbone of very large scale integration (VLSI)
  It is considered preferable to BJT technology for many applications.
note: MOSFET is more widely used in implementation of modern electronic devices
Notes: Note that MOSFETs are more recent development than Bipolar transistors.
Bipolar transistors were just beginning to be covered in EE curricula when I was in school (early 1960’s).
There was no mention of MOSFETS in that period.

## Slide 27
Depletion-Type MOSFET Construction
The Drain (D) and Source (S) connect to the to n-type regions.
  The n-typed regions are connected via an n-channel.
  The n-channel is connected to the Gate (G) via a thin insulating layer of silicon dioxide (SiO2).
The n-type material lies on a p-type substrate that may have an additional terminal connection called the
Substrate (SS).

## Slide 28: Basic Operation and Characteristics
Figure: n-Channel depletion-type MOSFET with VGS = 0 V and applied voltage VDD.
Figure: Reduction in free carriers in a channel due to a negative potential at the gate terminal.

## Slide 29: Basic MOSFET Operation
A depletion-type MOSFET can operate in two modes:
Depletion and Enhancement modes

## Slide 30
D-Type MOSFET in Depletion Mode
  When VGS = 0 V, ID = IDSS
  When VGS < 0 V, ID < IDSS
  The formula used to plot the transfer curve still applies:
Depletion Mode: The characteristics are similar to a JFET.

## Slide 31
D-Type MOSFET in Enhancement Mode
VGS > 0 V
ID increases above IDSS
The formula used to plot the transfer curve still applies:
Enhancement Mode:
Note that VGS is now a positive polarity

## Slide 33
p-Channel D-Type MOSFET

## Slide 34
D-Type MOSFET Symbols

## Slide 35
E-Type MOSFET Construction
The Drain (D) and Source (S) connect to the to n-type regions.
The Gate (G) connects to the p-type substrate via a thin insulating layer of silicon dioxide (SiO2)
There is no channel!
The n-type material lies on a p-type substrate that may have an additional terminal connection called the Substrate (SS)

## Slide 36
Basic Operation of the E-Type MOSFET
VGS is always positive
As VGS increases, ID increases
As VGS is kept constant and VDS is increased, then ID saturates (IDSS) and the saturation level, VDSsat is reached
The enhancement-type MOSFET operates only in the enhancement mode.
36

## Slide 37
E-Type MOSFET Transfer Curve
To determine ID given VGS:
Where:
  VT = threshold voltage or voltage at which the MOSFET turns on
k, a constant, can be determined by using values at a specific point and the formula:
VDSsat can be calculated by:
37

## Slide 38
p-Channel E-Type MOSFETs
The p-channel enhancement-type MOSFET is similar to the n-channel, except that the voltage polarities and current directions are reversed.
38

## Slide 39
MOSFET Symbols
39

## Slide 40: Difference between JFET & MOSFET
D-MOSFET
Depletion type
E-MOSFET
Enhancement type
J-FET
The key difference between JFET and MOSFET is that the gate terminal in MOSFET is insulated from the channel. Because of this insulated gate, the input impedance of a MOSFET is many times higher than that of a JFET.

## Slide 41
VMOS Devices
VMOS (vertical MOSFET) increases the surface area of the device.
Advantages
VMOS devices handle higher currents by providing more surface area to dissipate the heat.
VMOS devices also have faster switching times.
41

## Slide 42
Advantages
Useful in logic circuit designs
Higher input impedance
Faster switching speeds
Lower operating power levels
CMOS Devices
CMOS (complementary MOSFET) uses a p-channel and n-channel MOSFET; often on the same substrate as shown here.
42