## Slide 1
Transistor: Construction and Operation

## Slide 2: Introduction
This chapter will help you to learn:
  The physical structure of the bipolar transistor and how it works.
  How the voltage between two terminals of the transistor controls the current that flows through the third terminal, and the equations that describe these current-voltage relationships.
  How to analyze and design circuits that contain bipolar transistors, resistors, and dc sources.
  How the transistor can be used to make an amplifier.
  The three basic ways for connecting a BJT to be able to construct amplifiers with different properties.
  How the transistor can be used to design switch (for example: logic circuits).

## Slide 3: Introduction
On December 23, 1947, Dr. S. William Shockley, Walter H. Brattain, and John Bardeen demonstrated the amplifying action of the first transistor at the Bell Telephone Laboratories.
In early 1948, Dr. S. William Shockley came up with refined transistor called the Bipolar Junction Transistor (BJT).
On June 30, 1948, Bell Labs officially announced the first transistor at a press conference in New York.
The first transistor used two closely spaced gold contacts pressed onto the surface of a slab of high-purity germanium
Shockley, Bardeen and Brattain shared the 1956 Nobel Prize in Physics for the transistor.

## Slide 4: Introduction
  A transistor is a three terminal device.
  It is used to amplify, Oscillates, or Switches the flow of current between two terminals.
  Advantages: Transistor has few advantages over tube devices
  Smaller and lightweight.
  No heater requirement.
  A rugged construction.
  Takes less power
  Require no warm-up period
  Lower operating voltages

## Slide 5: Applications of transistors
Transistor are mostly used than diodes because they can be used in a multitude of applications:
    signal amplification
    design of digital logic and memory circuits.

## Slide 6: Applications of transistor

## Slide 7: Transistor Material
The transistor is an arrangement of semiconductor materials that share common physical boundaries.
Materials most commonly used are
  Silicon (Si)
  Gallium-arsenide (GaAs)
  And germanium (Ge)

## Slide 8: Classification of Transistors
P-Channel
N-Channel
Enhancement
Junction Gate Field-Effect Transistor (JFET)
Metal Oxide Silicon Field Effect Transistor (MOSFET)
Depletion
N-Channel
P-Channel
P-Channel
N-Channel
Depletion
Transistor
Point Contact Transistor
Bipolar Junction Transistor (BJT)
Field Effect Transistor (FET)
NPN Transistor
PNP Transistor

## Slide 9: BJT Structure
0.150 in
0.001 in
0.001 in
0.150 in
Three terminals of transistors are E for emitter , C for collector , and B for base.
The abbreviation of bipolar junction transistor is BJT.
If only one carrier is employed (electron or hole), it is considered a unipolar device such as Field Effect Transistor (FET)
Since both electrons and holes participate in the injection process into oppositely polarized materials of transistor, it is called bipolar.
Width: C>E>B and Doping: E>C>B
PNP-type
NPN-type

## Slide 10: BJT Structure
Transistor consists of two pn-junctions:
  emitter-base junction (EBJ)
  collector-base junction (CBJ)
The arrow on schematic symbol is important because:
  Identify the component terminal
    The arrow is always drawn on the emitter terminal.
  The arrow always points toward n-type material
    If the arrow point toward base, transistor is pnp type. If it points toward emitter, transistor is npn type.
PNP-type
NPN-type

## Slide 11: BJT Structure

## Slide 12
    Active
    Operating range of the amplifier.
    Base-Emitter Junction forward biased.
    Collector-Base Junction reverse biased
    Cutoff
    The amplifier is basically off. There is voltage but little current.
    Both junctions reverse biased
    Saturation
    The amplifier is full on. There is little voltage but lots of current.
    Both junctions forward biased
Modes of Operation

## Slide 13: NPN Active Mode of Operation
Active mode is the “most important.”
Two external voltage sources are required for biasing to achieve it.
Applying Kirchhoff’s current law to the transistor,
The collector current is comprised of two currents:
Notes: VBE causes the p-type base to be higher in potential than the n-type emitter, thus forward-biasing the emitter–base junction. The collector–base voltage VCB causes the n-type collector to be at a higher potential than the p-type base, thus reverse-biasing the collector–base junction.

## Slide 14: NPN Cutoff Mode of Operation
+ VBE -
- VCB +
REVERSE-BIASED
REVERSE-BIASED
EMITTER
COLLECTOR
BASE
IE=0
IC=0
IB=0

## Slide 15: NPN Saturation Mode of Operation
- VBE +
+VCB -
FORWARD-BIASED
FORWARD-BIASED
EMITTER
COLLECTOR
BASE
IE
IC
IB0

## Slide 16: PNP Active Mode of Operation
Active mode is the “most important.”
Two external voltage sources are required for biasing to achieve it.
Applying Kirchhoff’s current law to the transistor,
Notes: VBE causes the p-type base to be higher in potential than the n-type emitter, thus forward-biasing the emitter–base junction. The collector–base voltage VCB causes the n-type collector to be at a higher potential than the p-type base, thus reverse-biasing the collector–base junction.

## Slide 17: PNP Cutoff Mode of Operation
- VEB +
+ VBC -
REVERSE-BIASED
REVERSE-BIASED
EMITTER
COLLECTOR
BASE
IE=0
IC=0
IB=0

## Slide 18: PNP Saturation Mode of Operation
+ VEB -
- VBC +
FORWARD-BIASED
FORWARD-BIASED
EMITTER
COLLECTOR
BASE
IE
IC
IB0

## Slide 19: BJT Configuration
In the electronic circuit, there are three possible ways to connect BJT, where one terminal being common to both input and output signals.
  Common Base Configuration – has Voltage Gain but no Current Gain.
  Common Emitter Configuration – has both Current and Voltage Gain (most widely used).
  Common Collector Configuration – has Current Gain but no Voltage Gain

## Slide 20: Common Base Configuration
The base is common to both input (emitter–base) and output (collector–base) of the transistor.

## Slide 21: Common Base Configuration
I/P characteristics curve is plotted vs
O/P characteristics curve is plotted vs
Input
Weak Signal
Output
Amplified Signal
Here, for the biasing voltages:
EB diode is forward bias
BC diode is reversed bias
So,
Apply KCL,
Number of electrons reaching the collector region is directly proportional to the number of electrons injected or crossing the base region.
IC = dc IE
or
    Where, dc is called common base current gain
    Ideally:
    In reality: is between 0.9 and 0.998
Alpha () in the AC mode:

## Slide 22: Common Base Configuration
This curve shows the relationship between of input current (IE) to input voltage (VBE) for three output voltage (VCB) levels.
Input Characteristics:
Input
Weak Signal
Output
Amplified Signal

## Slide 23: Common Base Configuration
Output Characteristics
This graph demonstrates the output current (IC) to an output voltage (VCB) for various levels of input current (IE).
IC = dc IE

## Slide 24
Transistor Amplification
Voltage Gain:
if we assume
Currents and Voltages:
S
S

## Slide 25
Common–Emitter Configuration
The emitter is common to both input (base-emitter) and output (collector-emitter).
The input is on the base and the output is on the collector.
Notation and symbols used with the common-emitter configuration: (a) npn transistor; (b) pnp transistor.
i/p current-
i/p voltage-
o/p current-
o/p voltage-

## Slide 26
Common-Emitter Amplifier Currents
Ideal Currents: IE = IC + IB and IC =  IE
Actual Currents: IC =  IE + ICBO
where ICBO = minority collector current
      ICBO is usually so small that it can be ignored, except in high power transistors and in high temperature environments.
IC =  () + ICBO
Beta ()
 represents the amplification factor of a transistor. ( is sometimes referred to as hfe, a term used in transistor modeling calculations)
In DC mode:
In AC mode:

## Slide 27
Common-Emitter Amplifier Currents
Ideal Currents: IE = IC + IB and IC =  IE
Actual Currents: IC =  IE + ICBO
where ICBO = minority collector current
      ICBO is usually so small that it can be ignored, except in high power transistors and in high temperature environments.
IC =  () + ICBO
The collector current defined by the condition ,
Beta ()
 represents the amplification factor of a transistor. ( is sometimes referred to as hfe, a term used in transistor modeling calculations)
In DC mode:
In AC mode:

## Slide 28
A quantity , which represent the Relationship between and can be defined by
And amplification factor is given by,
Now, As we know,
Substitute, and into the above equations,
,
, and
Beta () provides a direct link between current levels of the input and output circuits for a common-emitter configuration. That is,
,
Relationship Between Alpha() Beta ()

## Slide 29
Common-Emitter Characteristics
Base Characteristics

## Slide 30
Common-Emitter Characteristics
Collector Characteristics
Ic=1.5 mA
vs for different level of
IC =  IE + ICBO
IC =
When,

## Slide 31
Determining  from a Graph
Beta ()

## Slide 32
Common–Collector Configuration
The input is on the base and the output is on the emitter.
Notation and symbols used with the common-collector configuration: (a) pnp transistor; (b) npn transistor.

## Slide 33
Common–Collector Configuration
The characteristics are similar to those of the common-emitter configuration, except the vertical axis is IE.

## Slide 34
VCE is at maximum and IC is at minimum (ICmax= ICEO) in the cutoff region.
IC is at maximum and VCE is at minimum (VCE max = VCEsat = VCEO) in the saturation region.
The transistor operates in the active region between saturation and cutoff.
Operating Limits for Each Configuration

## Slide 35
Power Dissipation
Common-collector:
Common-base:
Common-emitter:

## Slide 36
Transistor Specification Sheet

## Slide 37
Transistor Specification Sheet

## Slide 38
Transistor Testing
Curve Tracer
    Provides a graph of the characteristic curves.
DMM
    Some DMMs measure bDC or hFE.
Ohmmeter

## Slide 39
Transistor Terminal Identification