## Slide 1
BJTs-DC Biasing

## Slide 2: Introduction
The transistor is a magical device that can raise the level of the applied ac input without the assistance of an external energy source.
In actuality, the improved output ac power level is the result of a transfer of energy from the applied dc supplies.
The analysis or design of any electronic amplifier therefore has two components: the dc portion and the ac portion.

## Slide 3
Biasing
Biasing:
External dc voltages are applied to ensure that transistor can operate in the desired regions for desired applications is called biasing.
  For amplifier application, transistor should operate in active region
  For switch application, it should operate in cut-off and saturation.

## Slide 4
Biasing
Why do we need biasing?
One fundamental function of transistor is amplification. For faithful amplification, the transistor needs to be operated in active mode:
      Emitter-Base junction forward biased
      Collector-Base junction reverse biased
      To operate in the desired mode
      To stabilize the operating point (Q-point) against the changes in temperature, variations in transistor parameters, aging of the components etc.

## Slide 5
Operating Point
The Q-Point the combination of IC and VCE on the dc load line where a transistor has no input signal (Quiescent – at rest)
For transistor amplifiers the resulting dc currents and voltages (, and ) establish an operating point, Since the operating point is a fixed point on the characteristics, it is also called the quiescent point (abbreviated Q-point).
Hence, biasing is nothing but setting up a Q-point of the transistor near the middle of the dc load line.

## Slide 6
If no bias were used, the device would initially be completely off, resulting in a Q-point at A. Since it is necessary to bias a device so that it can respond to the entire range of an input signal, point A would not be suitable.
For point B, if a signal is applied to the
circuit, the device will vary in current and voltage from operating point, but not enough to drive the device into cutoff or saturation.
Point C would allow some positive and negative variation of the output signal, but the peak-to-peak value would be limited by the proximity of VCE=0
Point D sets the device operating point near the maximum voltage and power level. The output voltage swing in the positive direction is thus limited if the maximum voltage is not to be exceeded.
Point B therefore seems the best operating point in terms of linear gain and largest possible voltage and current swing.
Operating Point

## Slide 7
The Three States of Operation
    Active or Linear Region Operation
    Base–Emitter junction is forward biased
        Base–Collector junction is reverse biased
    Cutoff Region Operation
    Base–Emitter junction is reverse biased
    Saturation Region Operation
    Base–Emitter junction is forward biased
    Base–Collector junction is forward biased

## Slide 8
DC Biasing Circuits
Fixed-bias circuit or Base-bias
Emitter-stabilized bias circuit
Voltage divider bias circuit
DC bias with voltage feedback

## Slide 9: Fixed Biasing Circuit
For Fixed Bias Configuration:
Draw Equivalent Input circuit
Draw Equivalent Output circuit
Write necessary KVL and KCL Equations
Determine the Quiescent Operating Point
  Graphical Solution using Load lines
  Computational Analysis
Design and test design using a computer simulation

## Slide 10
Fixed Bias Circuit
A fixed bias has both ac and dc signal, to find the Q-point we will first DC analysis the network.
For the dc analysis the network can be isolated from the indicated ac levels, by replacing the capacitors with an open circuit equivalent.
for dc signal f=0 Hz
In addition, the dc supply VCC can be separated into two supplies (for analysis purposes only)

## Slide 11
The Base-Emitter Loop:
From Kirchhoff’s voltage law:
Solving for base current:
+VCC – IBRB – VBE = 0
Fixed Bias Circuit
Collector-Emitter Loop:
Since:
Using Kirchhoff's voltage law:
Because:
Since then:
And
Also:
with then:
As VCC is of fixed value, on selection of RB, the base current IB is fixed. Therefore this type is called fixed bias type of circuit.

## Slide 12
Fixed Bias Circuit
Determine the following for the fixed-bias configuration.
a. IBQ and ICQ.
b. VCEQ.
c. VB and VC .
d. VBC .

## Slide 13
Fixed Bias Circuit
Determine the following for the fixed-bias configuration.
a. IBQ and ICQ.
b. VCEQ.
c. VB and VC .
d. VBC .
The negative sign reveals that the junction is reversed-biased, as it should be for linear amplification.

## Slide 14: Stabilization
Stabilization: The process of making operating point independent of temperature changes and variations in transistor parameters is known as stabilization.
Causes of unstabilization of Q-point: Q-point will shift if either increases or decreases
    Change in
    IC = + (β+1)ICO
    Change in temperature
        increasing of every 10o temperature, is doubled
        Every degree rise in temperature the input voltage is decreased by 2.5 mV. The changes of affects the base current.

## Slide 15: The Thermal Stability of Operating Point (S)
Stability Factor (S):-
The stability factor is a measure of stability provided by biasing circuit.
Stability factor indicates the degree of change in operating point due to variation in temperature.
Stability factor should have the values as minimum as possible.
Definition: It is the rate of change of collector current with respect to the reverse saturation current , keeping β and constant.
The Thermal Stability Factor : at constant and β
at constant and β
at constant and
Larger the value of S, greater the thermal instability. This equation signifies that Changes S times as fast as

## Slide 16: The Thermal Stability of Operating Point (S)
The stability factor can be determined by differentiating the equation of Collector Current, IC = + (β+1)ICO, with respect to
Now,
Hence the stability factor S depends on β, IB and IC

## Slide 17: Stability Factor of Fixed Bias
Stability Factor (S),
As we know,
When changes by , and are unaffected
, is not present in the equation
Here, we can see that stability factor of fixed bias only depends on ,and fixed bias has large S indicates high un-stability.

## Slide 18
Pros and Cons of Fixed bias:
  Pros:
        Simple circuit
        Uses very few resistors
  Cons: Q-point is unstable
        If temperature increases, then β increases, and hence ICQ and VCEQ vary (effectively Q-point shifts)
        If the transistor is replaced with another transistor having different β value, then also Q-point shifts
          Usage:
                Due to the above inherent drawbacks, fixed bias is rarely used in linear circuits.
                Instead, it is often used in circuits where transistor is used as a switch.
Fixed Bias Circuit

## Slide 19
Saturation
When the transistor is operating in saturation, current through the transistor is at its maximum possible value.

## Slide 20: Determining ICsat
Determining ICsat for the fixed-bias configuration.
When

## Slide 21
Load Line Analysis
ICsat
  IC = VCC / RC
  VCE = 0 V
VCEcutoff
  VCE = VCC
  IC = 0 mA
  This line called the load line, since it is defined by the load resistance Rc
Where IB intersects with the load line we have the Q-point
  Q-point is the particular operating point:
  Value of RB
  Sets the value of IB
  Where IB and Load Line intersect
  Sets the values of VCE and IC.
The end points of the load line are:

## Slide 22
Circuit Values Affect the Q-Point
If the level of IB is changed by varying the value of RB the Q-point moves up or
down the load line

## Slide 23
Circuit Values Affect the Q-Point
Effect of increasing levels of RC on the load line and Q-point.

## Slide 24
Circuit Values Affect the Q-Point
Effect of lower values of VCC on the load line and Q-point.

## Slide 26
For the Emitter Stabilized Bias Configuration:
Draw Equivalent Input circuit
Draw Equivalent Output circuit
Write necessary KVL and KCL Equations
Determine the Quiescent Operating Point
  Graphical Solution using Load lines
  Computational Analysis
Design and test design using a computer simulation
Emitter-Stabilized Bias Circuit

## Slide 27
Emitter-Stabilized Bias Circuit
Adding a resistor (RE) to the emitter circuit stabilizes the bias circuit over fixed bias
BJT bias circuit with emitter resistor
DC equivalent circuit

## Slide 28
Base-Emitter Loop
From Kirchhoff’s voltage law:
Since IE = (b + 1)IB:
Solving for IB:

## Slide 29
Collector-Emitter Loop
From Kirchhoff’s voltage law:
Since IE  IC:
Also:

## Slide 30
Stability Factor for Emitter Bias Circuit
Adding RE to the emitter improves the stability of a transistor.
We know, for emitter bias circuit,
If we differentiate the first equation with respect to we get
Substitute the value of in the second equation.
If we consider ,
This circuit achieves good stability of dc operating point against changes in β with the help of emitter resistor which causes degeneration to take place.

## Slide 31
Pros and Cons of Emitter Stabilized Circuit:
  Pros:
        The circuit has the tendency to stabilize operating point against changes in temperature and β-value.
  Cons:
        As β-value is fixed for a given transistor, this relation can be satisfied either by keeping RE very large, or making RB very low.
        If RE is of large value, high VCC is necessary. This increases cost as well as necessary precautions while handling. a switch.
Emitter-Stabilized Bias Circuit

## Slide 34
Saturation Level
VCEcutoff:
ICsat:
The endpoints can be determined from the load line.

## Slide 35: Load line Analysis for Emitter Stabilized Bias Circuit
The collector-emitter loop equation that defines the load line is:
Choosing IC = 0 gives
And choosing VCE = 0 gives

## Slide 36: Load line Analysis for Emitter Stabilized Bias Circuit
Problem:
    Draw the load line for the network of Fig. (a) on the characteristics for the transistor appearing in Fig. (b).
    For a Q -point at the intersection of the load line with a base current of 15 m A , find the values of ICQ and VCEQ.
    Determine the dc beta at the Q-point.
    Using the beta for the network determined in part c, calculate the required value of RB and suggest a possible standard value.

## Slide 37
Solution:
(a) Two points on the characteristics are required to draw the load line.
(b) From the characteristics curve,
we find
(c) The resulting dc beta is:
(d)

## Slide 38
Voltage Divider Bias
This is a very stable bias circuit.
The currents and voltages are nearly independent of any variations in , since it is temperature sensitive especially for silicon transistors
1st step: Locate capacitors and replace them with an open circuit

## Slide 39
2nd step: Simplify the circuit using Thevenin Theorem
From Thevenin’s Theorem
Voltage Divider Bias

## Slide 40
3rd step: Locate 2 main loops.
1
2
BE Loop
1
CE Loop
2
Voltage Divider Bias

## Slide 41
BE Loop Analysis:
1
From KVL:
But
Voltage Divider Bias

## Slide 42
2
From KVL:
Assume
IC  IE
Voltage Divider Bias

## Slide 43: DC load line with Voltage Divider Bias
The dc load line can be drawn from the following equation:
IC
VCC
VCE

## Slide 44
Example: Determine the exact and the approximate dc bias voltage VCE and the current IC for the following voltage-divider configuration:

## Slide 45
Stability Factor for Voltage Divider Bias
Provides good Q-point stability with a single polarity supply voltage
We know, for voltage divider bias circuit,
If we differentiate the current with respect to we get
Substitute the value of in the second equation.
If we consider ,
Here we can see that stability factor independent of β. So, the operating point remains where it is fixed.

## Slide 46
Pros and Cons of Emitter Stabilized Circuit:
  Pros:
        Operating point is almost independent of β variation.
        Operating point stabilized against shift in temperature..
  Cons:
        As β-value is fixed for a given transistor, this relation can be satisfied either by keeping RE fairly large
        If is Small, circuit will draw more current from , which reduce the battery life.
        If RE is of large value, high VCC is necessary.
        This increases cost as well as precautions necessary while handling.
          Usage:
                Widely used in linear circuits .
Voltage Divider Bias Circuit

## Slide 47
Voltage Divider Bias Analysis
Transistor Saturation Level
Load Line Analysis
  Cutoff: Saturation:

## Slide 48
Collector Feedback Configuration
Another way to improve the stability of a bias circuit is to add a feedback path from collector to base.
In this bias circuit the Q-point is only slightly dependent on the transistor beta, .

## Slide 49
Base-Emitter Loop
From Kirchhoff’s voltage law:
Where IB << IC:
Knowing IC = IB and IE  IC, the loop equation becomes:
Solving for IB:

## Slide 50
Collector-Emitter Loop
Applying Kirchhoff's voltage law:
IE RE+ VCE + I’CRC – VCC = 0
Since IC  IC and IC = IB:
IC(RC + RE) + VCE – VCC =0
Solving for VCE:
VCE = VCC – IC(RC + RE)

## Slide 51
Stability Factor for Collector Feedback Configuration
Provides good Q-point stability with a single polarity supply voltage
We know, for collector feedback configuration,
If we differentiate the current with respect to we get
Substitute the value of in the second equation.
If we consider ,
This circuit achieves good stability of dc operating point against changes in β.

## Slide 52
Pros and Cons of Emitter Stabilized Circuit:
  Pros:
        Operating point is almost independent of β variation.
        Operating point stabilized against shift in temperature..
  Cons:
        As β-value is fixed for a given transistor, this relation can be satisfied either by keeping RE fairly large
        If is Small, circuit will draw more current from , which reduce the battery life.
        If RE is of large value, high VCC is necessary.
        This increases cost as well as precautions necessary while handling.
Collector Feedback Configuration

## Slide 53
Base-Emitter Bias Analysis
Transistor Saturation Level
Load Line Analysis
  Cutoff: Saturation:

## Slide 54
Determine the quiescent levels of ICQ and VCEQ for the network
EXAMPLE

## Slide 55
Design Operations
Given the device characteristics of Fig. a , determine VCC, RB, and RC for the fixed-bias configuration of Fig. b

## Slide 56
Design Operations
Given that ICQ = 2 mA and VCEQ = 10 V, determine R1 and RC for the following network.
The nearest standard commercial values to R1 are 82 kΩ and 91 kΩ . However, using the series combination of standard values of 82 kΩ and 4.7 kΩ, 86.7 kΩ would result in a value very close to the design level.

## Slide 57
Design Operations
The emitter-bias configuration of the following figure has the following specifications: ICQ = 1/2Isat, ICsat = 8 mA, VC = 18 V, and 110. Determine RC , RE , and RB.

## Slide 58
Design Operations

## Slide 59
Transistor Switching Networks
Transistors with only the DC source applied can be used as electronic switches.

## Slide 60
Switching Circuit Calculations
Saturation current:
To ensure saturation:
Emitter-collector resistance at saturation and cutoff:

## Slide 61
Switching Circuit Calculations
Determine RB and RC for the transistor inverter of the following figure if ICsat = 10 mA.

## Slide 62
Switching Time
Transistor switching times:

## Slide 63
PNP Transistors
The analysis for pnp transistor biasing circuits is the same as that for npn transistor circuits. The only difference is that the currents are flowing in the opposite direction.